Tabulated Summary of the Speed Camera Data for Moor Road, Rasen Road & Walesby Hill

	Moor Road / 08/11/22 - 21/11/22	Rasen Road / 22/11/22 - 04/01/23	Walesby Hill / 06/01/23 - 24/01/23
Average Speed (mph)	25.4	24.1	28.1
85th Percentile / (See below) (mph)	32.1	30.3	33.8
Maximum Speed (mph)	50	55	55

% of Speed Readings over 30mph	22	15	34
Average Speed of Readings over 30mph	34	34	34

Average Daily Vehicle Volume Count	274	220	214

The 85th Percentile is a statistical measure of the speed at and below which 85% of the vehicles within a measurement sample are travelling. It’s typically associated with the setting of speed limits, and (more controversially) often used as an argument against lowering them, or enforcing limits.
As you would expect there is a lot of information on the 85th Percentile with regards to the calculation method, use of, etc. on the internet for those interested.

The following pages show a Vehicle Count vs. Speed Histogram and a Plot of the Percentile Count vs Speed for all three locations.

Moor Road: Vehicle Count vs. Speed Histogram. 08/11/22 - 21/11/22

Moor Road: Plot of Percentile Counts vs. Speed. 08/11/22 - 21/11/22

Rasen Road: Vehicle Count vs. Speed Histogram. 22/11/22 – 04/01/23

Rasen Road: Plot of Percentile Counts vs. Speed. 22/11/22 - 04/01/23

Walesby Hill: Vehicle Count vs. Speed Histogram. 06-01-23 – 24/01/23

Walesby Hill: Plot of Percentile Counts vs. Speed. 06/01/23 - 24/011/23